*NOTE:  Prior to installation, please verify this kit is what you ordered. Clutch Kits returned which are found to be incorrect must be exactly as you received them. Kits that are modified in any way will not be accepted.

*NOTE:  It is imperative this kit be installed by a qualified technician and that all clearances and preload are followed exactly. If not followed as described, premature clutch wear will occur and damage to internal case components could occur. The seller is not responsible for improper installation or misuse of this product and will not be held liable.

*NOTE:  These instructions cover the recommended installation of the parts contained in this kit.  It is not intended as a guide in rebuilding the differential assembly as a whole.  For additional information on the differential assembly, it’s recommended the customer consult the manufacturer’s service manual.

Inventory - This kit contains the following parts:

14 Clutch Discs (8 tabbed and 6 splined)

12 Selective Shims

Recommended Tools/Fluids

80W90 Non Synthetic Petroleum Based Gear Lubricant

USE OF SYNTHETIC LUBRICANT VOIDS WARRANTY!!!

1.  Remove the cross shaft, s-spring, pinion gears, and thrust washers from the case and set aside.  These parts will be used again.

2.  Remove axle side gears, factory clutch discs and shims.  Remove the clutch discs and shims, from the side gears.  Save the factory shims and set the factory clutch discs and to the side.  The factory discs will not be used in the installation of the 8.5 Posi Clutch Kit.

3.  Remove the 14 clutch discs provided with the kit and clean thoroughly with Brake Cleaner. Then coat the clutch discs with a thin and even amount of 90 weight Petroleum Based Conventional gear oil.

4.  With both axle side gears face up (splined side up), start with an eared clutch disc and alternate with a splined clutch disc until each side gear has a total of 7 discs installed (4 tabbed and 3 splined).  Properly installed, you will start and end with a tabbed disc.

5.  Take the factory shims (there should be two; one for each side gear) that were removed and set aside in step 2 and install one on top of each side gear clutch pack. The shims are always stacked on the last tabbed clutch. The shims are always situated between the last clutch and the  case.

6.  Carefully install each side gear with its compliment of clutch discs and shim(s) in the case, ensuring the ears are properly lined up in the machined slots in the case.

7.  Install both pinion gears and thrust washers. Oil the thrust washers. Be sure that the pinion gears are aligned correctly. This will ensure that the cross shaft is seated properly.

WARRANTY:  Clutch Discs and related parts are free from defects in material and workmanship. Due to the intended use of these products, user assumes all risk and liability in connection with structural failure and malfunction of these products. Clutch Kits are to be installed by an automotive professional. We will not be responsible for product malfunction as a result of improper installation.